## Slide 1: Operating Systems Overview of HW architectures
Giuseppe Lipari

## Slide 2: Basic blocks
CPU
BUS
Main
Memory
Other I/O
devices
Disk
keyboard
Video

## Slide 3: The processor
Set of registers
  IP: instruction pointer
  SP: stack pointer
  A0-A3: general registers
  CR: control register
Execution units
  Arithmetic unit
  Fetching unit
  Branch prediction unit
  ...
Other components
  Pipeline
  Cache
CPU
IP
SP
R0
R1
R2
R3
Execution
Units
CR

## Slide 4: Processor registers
User visible registers
  Used as temporary buffers for processor operations
  Can be in any number
    RISC architectures: array of registers
    CISC architectures: set of registers dedicated to specific operations
Control and Status registers
  IP Instruction pointer
  SP Stack Pointer
  CR Control Register (or PSW Program Status Word)‏

## Slide 5: Modes of operation
Many processors have at least two modes of operation
  Supervisor mode
    All instructions are allowed
    Kernel routines execute in supervisor mode because the OS must access all features of the system
  User mode
    Not all instructions are allowed
    User programs execute in user mode
    Some instruction (for example, disabling interrupts) cannot be invoked directly by user programs
Switching
  It is possible to switch from user mode to supervisor mode with special instructions

## Slide 6: Main Memory and bus
The RAM
  Sequence of data locations
  Contains both instructions (TEXT) and data variables
The bus
  A set of “wires”
    Address wires
    Data wires
  The number of data wires is the amount of bits that can be read with one memory access
    Current PC buses: 32 bits, 64 bits

## Slide 7: Instruction execution
We distinguish at least two phases
  Fetching: the instruction is read from memory
  Execute: the instruction is executed
    Data processing instr. – the result is stored in registers
    Load instr. – the data is loaded from main memory
    Store – the data is stored in main memory
    Control – the flow of execution may change (change IP)‏
  Some instruction may be the combination of different types
Start
Halt
Fetch next
instruction
Execute
instruction

## Slide 8: Stack Frames
Stack
Frame
The stack is used to
  Save local variables
  Implement function calling
Every time a function is called
  The parameters are saved on the stack
  Call <address>: The current IP is saved on the stack
  The routine saves the registers that will be modified on the stack
  The local variables are defined on the stack
  When the function is over the stack is cleaned and the RET instruction is called which restores IP
Stack
Parameters
IP
R0
R1
R2
x
y

## Slide 9: External devices
I/O devices
  Set of data registers
  Set of control registers
  mapped on certain memory locations
D0
CR0
CR1
CR2
D1
D2
I/O device interface
BUS
CPU
IP
SP
R0
R1
R2
R3
CR
Memory
A3B0
A3B2
A3B4
A3B6
A3B8
A3BA
A3BC
…
FF00
FF02
FF04
FF06
FF08
FF0A

## Slide 10: I/O operations
Structure of an I/O operation
  Phase 1: prepare the device for the operation
    In case of output, data is transferred to the data buffer registers
    The operation parameters are set with the control registers
    The operation is triggered
  Phase 2: wait for the operation to be performed
    Devices are much slower than the processor
    It may take a while to get/put the data on the device
  Phase 3: complete the operation
    Error checking
    Clean up the control registers

## Slide 11: Example of input operation
Phase 1: nothing
Phase 2: wait until bit 0 of CR0 becomes 1
Phase 3: read data from D0 and reset bit 0 of CR0
BUS
CPU
IP
SP
R0
R1
R2
R3
CR
D0
CR0
CR1
CR2
D1
D2
I/O device interface
FF00
FF02
FF04
FF06
FF08
FF0A
CR0
D0
CR0
D0
R0

## Slide 12: Example of output operation
Phase 1: write data to D1 and set bit 0 of CR1
Phase 2: wait for bit 1 of CR1 to become 1
Phase 3: clean CR1
BUS
CPU
IP
SP
R0
R1
R2
R3
CR
D0
CR0
CR1
CR2
D1
D2
I/O device interface
FF00
FF02
FF04
FF06
FF08
FF0A
CR1
D1
D1
R0
CR1
R0
CR1

## Slide 13: Temporal diagram
Polling
  This technique is called “polling” because the processor “polls” the device until the operation is completed
  In general, it can be a waste of time
  The processor could execute something useful while the device is working
    but, how can the processor know when the device has completed the I/O operation?

## Slide 14: Interrupts
Every processor supports an interrupt mechanism
  The processor has a special pin, called “interrupt request (IRQ)”
  Upon reception of a signal on the IRQ pin,
    If interrupts are enabled, the processor suspends execution and invokes an “interrupt handler” routine
    If interrupts are disabled, the request is pending and will be served as soon as the interrupts are enabled
Start
Halt
Fetch next
instruction
Execute
instruction
Interrupts?
Serve
Interrupt

## Slide 15: Interrupt handling
Every interrupt is associated one “handler”
When the interrupt arrives
  The processor suspend what is doing
  Pushes CR on the stack
  Calls the handler (pushes the IP on the stack)‏
  The handler saves the registers that will be modified on the stack
  Executes the interrupt handling code
  Restores the registers
  Executes IRET (restores IP and CR)
Stack
CR
IP
R0
R1

## Slide 16: Input with interrupts
Phase 1: do nothing
Phase 2: execute other code
Phase 3: upon reception of the interrupt, read data from D0, clean CR0 and return to the interrupted code
BUS
CPU
IP
SP
R0
R1
R2
R3
CR
D0
CR0
CR1
CR2
D1
D2
I/O device interface
FF00
FF02
FF04
FF06
FF08
FF0A
CR0
D0
CR0
D0
R0
IRQ

## Slide 17: Interrupts
Let’s compare polling and interrupt
Normal
code
Interrupt
handler
Phase 1
Phase 2
Phase 3
Polling
code

## Slide 18: The meaning of phase 3
Phase 3 is used to signal the device that the interrupt has been served
  It is an handshake protocol
    The device signals the interrupt
    The processor serves the interrupt and exchanges the data
    The processor signals the device that it has finished serving the interrupt
    Now a new interrupt from the same device can be raised

## Slide 19: Interrupt disabling
Two special instructions
  STI: enables interrupts
  CLI: disables interrupts
  These instructions are privileged
    Can be executed only in supervisor mode
  When an interrupt arrives the processor goes automatically in supervisor mode
Normal
code
Interrupt
handler
CLI
STI
Pending
Interrupt

## Slide 20: Many sources of interrupts
Usually, processor has one single IRQ pin
  However, there are several different I/O devices
  Intel processors use an external Interrupt Controller
    8 IRQ input lines, one output line
BUS
CPU
IRQ
IRQ0
IRQ1
IRQ2
IRQ3
IRQ4
IRQ5
IRQ6
IRQ7
I/O
Device
I/O
Device
Interrupt
Controller

## Slide 21: Nesting interrupts
Interrupt disabling
  With CLI, all interrupts are disabled
When an interrupt is raised,
  before calling the interrupt handler, interrupts are automatically disabled
  However, it is possible to explicitely call STI to re-enable interrupts even during an interrupt handler
  In this way, we can “nest interrupts”
    One interrupt handler can itself be interrupted by another interrupt

## Slide 22: Interrupt controller
Interrupts have priority
  IRQ0 has the highest priority, IRQ7 the lowest
When an interrupt from a I/O device is raised
  If there are other interrupts pending
    If it is the highest priority interrupt, it is forwarded to the processor (raising the IRQ line)‏
    Otherwise, it remains pending, and it will be served when the processor finishes serving the current interrupt

## Slide 23: Nesting interrupts
Why nesting interrupts?
  If interrupts are not nested, important services many be delayed too much
    For example, IRQ0 is the timer interrupt
    The timer interrupt is used to set the time reference of the system
    If the timer interrupt is delayed too much, it can get lost (i.e. another interrupt from the timer could arrive before the previous one is served)‏
    Losing a timer interrupt can cause losing the correct time reference in the OS
    Therefore, the timer interrupt has the highest priority and can interrupt everything, even another “slower” interrupt

## Slide 24: Nested interrupts
Normal
code
Slow Interrupt
handler
High priority
Interrupt handler

## Slide 25: Atomicity
An hardware instruction is atomic if it cannot be “interleaved” with other instructions
  Atomic operations are always sequentialized
  Atomic operations cannot be interrupted
    They are safe operations
    For example, transferring one word from memory to register or viceversa
  Non atomic operations can be interrupted
    They are not “safe” operations
    Non elementary operations are not atomic

## Slide 26: Non atomic operations
Consider a “simple” operation like
x = x+1;
In assembler
LD R0, x
INC R0
ST x,RO
A simple operation like incrementing a memory variable may consist of three machine instructions
If the same operation is done inside an interrupt handler, an inconsistency can arise!

## Slide 27: Interrupt on non-atomic operations
int x=0;
...
x = x + 1;
...
Normal code
void handler(void)‏
{
...
x = x + 1;
....
}
Handler code
...
LD R0, x
INC R0
ST x, RO
...
Save registers
...
LD R0, x
INC R0
ST x, RO
...
Restore registers
?
R0
0
x
CPU
memory
0
Saved registers
0
0
1
1
0
1
1

## Slide 28: Solving the problem in single processor
One possibility is to disable interrupts in “critical sections”
...
CLI
LD R0, x
INC R0
ST x, RO
STI
...
Save registers
...
LD R0, x
INC R0
ST x, RO
...
Restore registers

## Slide 29: Multi-processor systems
Symmetric multi-processors (SMP)‏
  Identical processors
  One shared memory
CPU 0
CPU 1
CPU 2
CPU 3
Memory

## Slide 30: Multi-processor systems
Two typical organisations
  Master / Slave
    The OS runs on one processor only (master), CPU0
    When a process requires a OS service, sends a message to CPU0
  Symmetric
    One copy of the OS runs indipendentely on each processor
    They must synchronise on common data structures
    We will analyse this configuration later in the course

## Slide 31: Low level synchronisation in SMP
The atomicity problem cannot be solved by disabling the interrupts!
  If we disable the interrupts, we protect the code from interrupts.
  It is not easy to protect from other processors
...
LD R0, x
INC R0
ST x, RO
...
...
LD R0, x
INC R0
ST x, RO
...
...
LD R0, x (CPU 0)‏
LD R0, x (CPU 1)‏
INC R0 (CPU 0)‏
INC R0 (CPU 1)‏
ST x, R0 (CPU 0)‏
ST x, R0 (CPU 1)‏
...
CPU 0
CPU 1

## Slide 32: Low level synchronisation in SMP
Most processors support some special instruction
  XCH Exchange register with memory location
  TST If memory location = 0, set location to 1 and return true (1), else return false (0)‏

## Slide 33: Pseudo-code for TST and XCH
XCH and TST
are atomic!
void xch(register R, memory x)‏
{
int tmp;
tmp = R; R = x; x=tmp;
}
int tst(int x)‏
{
if (x == 1) return 0;
else {
x=1;
return 1;
}
}

## Slide 34: How they work
XCH and TST
  the processor that executes the instruction locks the bus and performs two operations (read and write) without interference from other processors
  needs a bus arbiter

## Slide 35: Locking in multi-processors
We define one variable s
  If s == 0, then we can perform the critical operation
  If s == 1, the must wait before performing the critical operation
Using XCH or TST we can implement two functions:
  lock() and unlock()‏

## Slide 36: Locking with XCH
Since there is an active waiting, this technique is called spinlock
void lock(int s)‏
{
int a = 1;
while (a==1) XCH (s,a);
}
void unlock(int s)‏
{
s = 0;
}
; ------------------------------
; LOCK(S)‏
; ------------------------------
LD R0,1
LABEL : XCH R0, s
CMP R0, 1
JE LABEL
...
; ------------------------------
; UNLOCK(S)‏
; ------------------------------
LD R0, 0
LD s, R0
...

## Slide 37: Locking with TST
void lock(int x)‏
{
while (TST (s) == 0);
}
void unlock(int s)‏
{
s = 0;
}
; --------------------------------
; LOCK
;---------------------------------
LABEL: TST s
JZ LABEL
....
; ------------------------------
; UNLOCK(S)‏
; ------------------------------
LD R0, 0
LD s, R0
...
Again an active waiting, this is a different implementation of the spinlock

## Slide 38: Locking in multi-processors
L0: TST s
JZ L0
LD R0, x
INC R0
ST x, R0
LD R1, 0
ST s, R1
...
TST s (CPU 0)‏
TST s (CPU 1)‏
JZ L0 (CPU 0)‏
JZ L0 (CPU 1)‏
LD R0, x (CPU 0)‏
TST s (CPU 1)‏
INC R0 (CPU 0)‏
JZ L0 (CPU 1)‏
ST x, R0 (CPU 0)‏
TST s (CPU 1)‏
LD R1, 0 (CPU 0)‏
JZ L0 (CPU 1)‏
ST s, R1 (CPU 0)‏
TST s (CPU 1)‏
... (CPU 0)‏
JZ L0 (CPU 1)‏
... (CPU 0)‏
LD R0, x (CPU 1)‏
CPU 0
CPU 1
L0: TST s
JZ L0
LD R0, x
INC R0
ST x, RO
LD R1, 0
ST s, R1
...
Lock(s)‏
Unlock(s)‏
Unlock(s)‏
Lock(s)‏
x=x+1
x=x+1

## Slide 39: Locking
The lock / unlock operations are “safe”
  No matter how you interleave the operations, there is no possibility that the “critical parts” interleave
  However, spinlock is an active wait and a possible wast of time
The problem of locking is very general and will be analysed and solved in greater details later

## Slide 40: Spinlock
Problem 1
  If CPU1 waits for CPU0 with a spinlock, it cannot execute other activities
  this is a waste of processor time
Problem 2
  When CPU1 waits for CPU0 with a spinlock, it accesses memory continuosly
  It occupies the system shared bus
  It slows down the other processors! (It reduces considerably the bus bandwidth)‏

## Slide 41: More sophisticated techniques
Using cache coherency
  if every processor has a local cache, a cache coherency algorithm ensures that the cache content is synchronized with the global memory
CPU0
CPU0
CPU1
s=0
s=0
s=0
s=1
1. Writes back to global memory
2. Invalidates cache line
s=0
s=1