## Slide 1: I/O subsystem
Giuseppe Lipari

## Slide 2: Input – Output and Device – Drivers

## Slide 3: Objectives of the I/O subsystem
To hide the complexity
From the variability of the devices
  Provide a consinstent API
    Open(), Read(), Write(), Close(), Lseek()‏
  Provide a naming system
    For example, the file system
  Optimize access
    For example, through buffering and caching

## Slide 4: Logical organisation
We can distinguish two logical levels
  Device – dependent level
    Strictly depends on the particular device
  Device – independent level
    Provides an uniform interface to the user
Application
Device – independent level
Device – dependent level
HW
Device
User – level
OS – level
HW – level

## Slide 5: Device - independent level
In this layer, the following functionalities are provided
  Buffering
    It is needed to transfer data to user space
    Used to optimize the reading/writing on a device
  Error handling
    Many different kind of errors!
    Errors can be reported to the user in a meaningful way
  Allocation and spooling
    How to allocate a device to a process requesting the service
    for example, printing, visualizing, input from the mouse/keyboard, etc.
  Naming
    Each device is assigned a logical “identifier”
    Data on the device can be accessed through the identifier

## Slide 6: Device – dependent level
In this level
  The device driver interacts directly with the HW
  It interacts also with the device-independent level
  It provides specific access modes to the device
  It provides ways to communicate with the upper layer
  The interface between the d-d layer and the d-i level is specific for the device
    Usually, it is a set of functions very similar to the user/level functions open(), read(), write(), close(), etc.

## Slide 7: Device drivers
A device drivers is
  a software module of the OS that contains code dedicated to the interaction with a particular device
    Disk device driver
    Keyboard device driver, etc.
Why device drivers
  Abstraction
  Portability
  Modularity of the OS code

## Slide 8: Variability
The device driver subsystem
  It is one of the most complex parts of the OS
  The complexity is due to the huge variability of devices
Classification of I/O devices
  Human readable
    mouse, keyboad, video, printer, etc.
  Machine readable
    Disk, controllers, sensors, actuators
  Communication
    digital networks, modems

## Slide 9: Characteristics of a device
Data rate
  There can be huge differences in the speed of data transfer
Applications
  the way in which a device is used is important to the device driver implementation
    for example, disk for normal user interaction, disk for web servers, disk for video servers, disk for virtual memory management, etc.
Complexity of control
  From very simple (e.g. the printer) to very complex (e.g. the disk)‏
Unit of transfer
  Character devices, block devices, packet devices
Data representation
  Parity, encoding, error corrections, etc.
Error conditions
  The way in which errors may occur, and the way they are reported may vary a lot

## Slide 10: I/O device controller
Let us start from the HW
Every device has a controller that consists of
  a dedicated small processor for I/O control
  a set of registers mapped in memory memory
Commands
  To send commands to a I/O device, write on the registers
  To read the status of the I/O operation, read from the registers
The CPU is NOT synchronised with the I/O processors!
  Data can arrive from the device in a asynchronous way

## Slide 11: Controller Registers
A device controller should posses at least the following registers
Control register CR
  It is used to send commands to the controller
    For example, start a output data transfer, start a input data transfer, etc
    We assume that a start bit is defined
Status Register SR
  It is used to check the status of the current operation and of the device
    For example, if the transfer has been completed, it an error occurred, etc.
    We assume that a flag bit is defined to signal to completion of any operation
It can have also a data register/buffer and a Configuration register

## Slide 12: External process
We can model the I/O controller as a process
  it is not a real software process! it is only a model for its behaviour
extrernal process {
while (true) {
while (start==0);
<execute command>
<update status register>
flag = 1;
}
}

## Slide 13: Character – based devices
First, we will discuss character based devices
  example, the keyboard, the serial line, etc
To transfer n bytes
  n different I/O operations
This is the simplest case

## Slide 14: Polling
In polling,
  the operating system directly checks the flag bits
  active waiting!
...
for (i=0; i<n; i++) {
<prepare transfer>
start = 1;
while (flag==0);
<check status>
}
…

## Slide 15: Polling
If the device is very fast, then polling may be the best approach
  In fact, an interrupt based mechanism involves at least a pair of process switches
  It the duration of the operation is less than two process switches, then polling is the most optimized solution
Almost all devices are much slower than the processor
  usually, a data transfer takes much more than two process switches
  For these devices, an interrupt-based mechanism is the best approach

## Slide 16: Interrupt based I/O
In the controller
  The controller interrupt mechanism must be configured
    We must specify which interrupt line is dedicated to the device
    Different devices send data on different interrupts lines
    All the lines enter in the interrupt controller
    The interrupt controller will rais the interrupt pin of the processor
In the processor
  The processor interrupt mechanism must be configured
    The processor has an “interrupt vector”
    For every interrupt line, the address of a function (interrupt handler) is specified
    When the interrupt is raised, the corresponding interrupt handler is invoked

## Slide 17: Interrupt handling mechanism
The device driver is written as a process
  It is a very special kind of process
  It is not a user process, but a kernel process, because it runs in the same address space of the operating system
  In the following, it will be called Internal Process, to distinguish from the external process
We define a semaphore available
  the internal process is blocked on available waiting for the completion of the operation
  when the interrupt handler executes, it performs the signal on available

## Slide 18: Interrupt handler
...
for (i=0; i<n; i++) {
<prepare transfer>
start = 1;
available.wait();
<check status>
}
...
Semaphore available(0);
void handler()‏
{
available.signal();
}
Interrupt handler
Internal process
external process {
while (true) {
while (start==0);
<execute command>
<update status register>
flag = 1;
<raise interrupt>
}
}
External process

## Slide 19: Temporal evolution

## Slide 20: Some intelligence in the handler
The previous structure has one drawback
  For each data byte, the internal process is executed
  This requires two process switches for every byte
Idea
  The transfer of subsequent bytes can be done by the interrupt handler itself!
Device descriptor
  It is a data structure shared by the internal process and the interrupt handler
  It contains a buffer of the data to be transferred

## Slide 21: Device descriptor
It contains
  A semaphore end_of_transfer, on which the internal process will be blocked
  The address of the device controller registers
    Status and control registers
  Number of bytes to be transferred
  Counter for number of transferred bytes
  Buffer address
    Where data is put or where data is taken
All device descriptors are kept in a array
  The array is indexed by the device identifier
  The devide identifier is an integer that identifies the device

## Slide 22: Device descriptor
struct IO_descr {
Semaphore end_of_transfer;
int counter;
int nbytes;
int *CR;
int *SR;
void *buffer;
int status;
// etc.
};
struct IO_descr dev_descr[NUM_DEVICES];

## Slide 23: Read operation
This function is invoked by the internal process
int read(int ddes, char *pbuf, int nbytes) {
dev_descr[ddes].nbytes = nbytes;
dev_descr[ddes].counter = 0;
dev_descr[ddes].buffer = pbuf;
<set start = 1>
dev_descr[ddes].end_of_transfer.wait();
<check status>
if (<error>)
< return error_code>
return dev_descr[ddes].counter;
}

## Slide 24: Interrupt handler
void handler() {
char b;
<check for error>
if (<no error>) {
*dev_descr[ddev].buffer = <get data from device>;
dev_descr[ddev].buffer++;
dev_descr[ddev].counter++;
if (dev_descr[ddev].counter < dev_descr[ddev].nbytes)
<set start bit = 1>
else
dev_descr[ddev].end_of_transfer.signal();
}
else {
if (<non critical error>)
<retry : set start bit = 1>
else
dev_descr[ddev].status = error_code
}
}

## Slide 25: Timing

## Slide 26: Direct memory access
Many I/O controllers support Direct Memory Access
  Every I/O controller has a DMA interface
    A memory address register (MAR)‏
    A counter
  It can automatically transfer a block of bytes to/from memory
  At the end of the transfer, an interrupt is raised
With DMA
  The interrupt handler becomes very simple!

## Slide 27
Memory
CPU
MAR
MCR
CR
ST
Interrupt

## Slide 28: Read operation
int read(int ddes, char *pbuf, int nbytes) {
dev_descr[ddes].nbytes = nbytes;
dev_descr[ddes].counter = 0;
dev_descr[ddev].buffer = pbuf;
<program DMA>
<MAR = pbuf>
<MCR = nbytes>
dev_descr[ddev].end_of_transfer.wait();
<check status>
if (<error>)
< return error_code>
return dev_descr[ddev].counter;
}

## Slide 29: Interrupt handler
void handler() {
<check for error>
if (<no error>) {
dev_descr[ddev].counter=<MCR>;
dev_descr[ddev].end_of_transfer.signal();
}
else {
if (<non critical error>)
<retry : set start bit = 1>
else
dev_descr[ddev].status = error_code
}
}

## Slide 30: DMA
By using DMA
  The overhead is further reduced
  The interrupt is called only once at the end of the operation
  The controller is more complex
Overhead
  The DMA transfers data to memory on the bus
  The bus and the memory are shared between the processor and the I/O device
  Conflicts on the bus are resolved by the bus controller
  However, the overhead of the DMA is not 0!
  Every read/write operation from/to memory can be delayd because the I/O device could access the memory at the same time!

## Slide 31: Buffering
Goals
Transfer data to user space
  Mechanism
    Data is first loaded into an internal buffer of the OS
    The, it is transferred into the user buffer
  Why
    For timing reasons: while reading one buffer, I can try to load another buffer
    For Virtual memory reasons: the memory of the process (which could be subject to swapping and paging) is not directly involved with the I/O hardware operation
Optimized access
  Instead of loading data wehn we need them, load them in advance

## Slide 32: Buffering
Single buffer
  One single buffer for each device
  While the operation is performed, the process cannot access the buffer
Double buffering
  Two buffers for each device
  While the operation is performed on one buffer, the other can be used by the process
  At the end of the reading, we can swap the buffers
Circular buffer
  An extension of the double buffering
  It is used only in particular cases

## Slide 33: Block devices
As an example of block devices, we will consider the disk

## Slide 34: Disk performance
Average transfer time TF = TA + TT
  The average access time TA is the time to move the disk arm to the desired track and sector
  The average byte transfer time TT is the time needed to actually transfer the data
TA = ST + RL
  the seek time ST is needed to move the arm on the desired trask
  the rotational latency RL is the time waiting for the disk to rotate until the desired sector
The greatest and most important time is the ST
  The arm moves more slowly than the disk rotate
GOAL:
  move the arm the less that is possible!

## Slide 35: Some data
Western Digital WDE18300
Cylinders: 13614
Tracks per cylinder: 8
Sectors per track: 320
Bytes per sector: 512
Capacity: 18.3 Gb
Times
  Minimum ST 0.6 msec
  Average ST 5.2 msec
  Rotational Latency RL 6 msec, (average 3 msec)‏
  Average transfer time TT 19 microsec.

## Slide 36: Example
Let’s compute the time to read a 320kb file
  Suppose that a process wants to read 640 sectors (320 kb)‏
  Assume they are stored in two consecutive tracks
    First Track:
      TF = ST + RL + TT = 5.2 + 3 + 6 = 14.2
    Second track
      TF = ST + RL + TT = 0.6 + 3 + 6 = 9.6
    Total : 23.8 msec
  Assume they are stored in random order
    Every sector
      TF = ST + RL + TT = 5.2 + 3 + 0.019 = 8.219
    Total: 8.219 * 640 = 5.26 seconds!!

## Slide 37: Scheduling
There is a huge difference in the two times
  It is much more convenient to store files consecutively
  However, there is a problem
  Several processes could request reading from the disk
  If we serve the requests as they come, we could end up moving the arm up and down even in the case the files are stored consecutively!

## Slide 38: FIFO
Example:
  Requests in the queue: 20, 14, 40, 23, 47, 7
  With FIFO, we have a very bad performance! (the arm keeps moving randomly)‏

## Slide 39: SSTF
Shortest Seek Time first
  Server the request that is closer to the actual position of the arm
  Requests in the queue: 20, 14, 40, 23, 47, 7
  Order of service: 20, 23, 14, 7, 40, 47

## Slide 40: SSTF: problems
The algorithm is not optimal
  Minimizing the seek time for the next reading does not imply minimizing the total seek time
  The algorithm could cause starvation!
  If the disk is in overload (too many requests), a request of a cyclinder that is far away never gets served!

## Slide 41: SCAN
It is called the “elevator algorithm”
  Keep increasing the cylinder search in one direction, then it changes direction
  Requests in the queue: 20, 14, 40, 23, 47, 7
  Order of service: 20, 14, 7, 23, 40, 47

## Slide 42: RAID
It is used for fault tolerant disks
  a virtual disk is implemented as a set of “real disks”

## Slide 43: 6 levels
RAID 0
  No redundancy: only for performance improvement
  data can be accessed in parallel!
RAID 1:
  Simple duplication, very costly
RAID 2:
  Hamming code: quite costly
RAID 3:
  One disk for parity (bit level)‏
RAID 4:
  Block level parity
RAID 5:
  Block level distributed parity
RAID 6:
  Dual Redundancy