Embedded Systems / Model-Based Design

Written exam – February 27 2013

Q1.

Compute the composition of machines A, B and C.

Q2.

Define the FSMs that realizes the following description.

The system has a binary input (values 0,1), a and two outputs c0 and c1. The pair c0 and c1 is the binary encoding modulo 4 of the number of pairs 1,0 received on the input a.

Q3.

Provide a C code implementation of the previous machine.

Q4.

Provide a set of input values that realizes boundary testing and robustness testing for the following system S.

The system S computes the minimum or maximum point (x,y) for the function y=ax2+bx+c where

a, b and c are integers with values in the ranges a([-10, 10], b([-100, 100], c([-200, 200]

# Text boxes

1/01

B2

B1

1/11

C2

C

0/01

0/0

1/0

0/1

B

1/00

1/1

A

B3

y

x

0/00

0/11

1/11

A2

0/10

A1

c

C1

1/01

0/10

b

a