Embedded Systems / Model-Based Design

Written exam – January 16 2014

Q1a. Compute the equivalent flat FSM

(partial solution)

Q1b. Write a segment of C code that implements it

Q2.

Write a test sequence with state and transition coverage for the following FSM.

R: the Transition tree (to compute the P set) is the following.

and the P set is the set of all the partial paths.

P= {(, 0, 1, 00, 01, 010, 011, 0100, 0101}

The separating sequences can be computed by noting that all states differ for their output with respect to at least one input, therefore r1 is already a partition of singletons.

This is clear if the output update function is expressed by a table

|  | 0 | 1 |
| --- | --- | --- |
| B1 | 0 | 0 |
| B2 | 1 | 0 |
| B3 | 1 | 1 |
| B4 | 0 | 1 |

The set W is W={0, 1}

and the set of test input sequences is rPxW = {r0, r1, r00, r01, r000, r001, r010, r011, r0100, r0101, r0110, r0111, r01000, r01001, r01010, r01011}

Q3.

Check if the A is an abstraction of B.

R: When computing the Simulation relation, the following state pairs are added

{ (B1, A1),

(B2, A2),     *because of the transition 0/0*

(B3, A3),      *because of the transition 1/0*

(B4, A2),      *because of 0/0*

At this point, for the transitions 1/1 from B3, there are these options

(B2, A3)   -   the algorithm fails because the transition 0/1 from B2 cannot be matched from A3

or

(B2, A1)   - again fails because of 0/1

indeed, the machine B has the possible behavior input=0110 - output 0011 that cannot be produced by A, therefore A is not an abstraction.

Alternatively, you may want to compute the output deterministic versions of A and B and compare them.

These are ...

Q3.

Define a set of functional tests for boundary testing and robustness testing.

# Text boxes

U1

0/0

1

B2

B4

0

1

B1

B1

1/1

0/1

B4

0/0

{A3}

1/0

1/1

1/0

0/0

D1

[vs>=u_th]

1/0

B3

1/1

B3

1/1

0/1

B

B2

1

B2

1/1

0

B1

0/0

1/1

1/1

[vs<=d_th]

B2

0/1

A

{A2}

{A1, A3}

B2

[vs<d_th]

[vs<u_th]

[vs<u_th]

[vs>u_th]

[vs>u_th]

[vs<d_th]

1

{A1}

B1

0

U1

1/0

[vs<=d_th]

0/1

[vs>d_th]

0/0

S2

D1

S1

[vs>d_th]

0/0

1/1

1/1

0

{B2, B3}

1/1