Embedded Systems / Model-Based Design

Written exam – February 10, 2014

Q1.

Given the autogenerated code in the attached listing.

Q1a. Reverse engineer it to derive the state machine that was used to generate it

Q1b. Write a test with guaranteed state and transition coverage for it

Q3.

Write a state machine B that refines A (and demonstrate that B is a refinement).

Q3.

Write a TLC block that generates code for the custom block SensorXX according to the following specification:

The sensor reads two double precision values x,y that are coordinates on a plane.

At initialization time, the sensor must be initialized by calling

InitializeSensor2D(x_range, y_range);

Providing the maximum range on the X and Y axis.

At runtime, the sensor must call the API function

ReadSensor2D(&x, &y);

With the addresses of two variables of type value that will contain the values.

# Text boxes

A3

00/0

00,01/1

11,11/0

10, 11/0

10/0

10/1

00,01/0

A3

00,11/1

00,10/1

00, 01/1

A

A2

11/0

A1

00/0